## Slide 1
Client - Broker Connection
with MQTT
Dr. Binil Starly
James T. Ryan Professor
Edward P. Fitts Department of Industrial & Systems Engineering
Notes: What iS MQTT? Design Principles, its Model – the Publish-Subscribe data Model, Operations and its Features

## Slide 2
7
Three Types of Participants
Broker
Publisher
Subscriber

## Slide 3
7
Hierarchical Organization of Data
Topics
Sub-Topics
Messages
Data Structure/Type

## Slide 4
Connection Flow
TCP connection
CONNECT
CONNACK
MQTT
Broker
MQTT
Client
Notes: What Types of Message Transfer Protocols are available ?

## Slide 5
CONNECT PACKET
MQTT CONNECT PACKET | 
Contains | Example
clientId | “machine-1”
cleanSession | True
username (optional) | “machineID”
password (optional) | “mysecretpwd”
lastWillTopic (optional) | “/machine1/temperature
lastWillQos (optional) | 2
lastWillMessage (optional) | “unexpected exit”
lastWillRetain (optional) | False
keepAlive (optional) | 60
Notes: What Types of Message Transfer Protocols are available ?

## Slide 6
CONNACK RESPONSE PACKET
MQTT CONNACK | 
Contains | Example
sessionPresent | True
returnCode | 0
Return Code | Return Code Response
0 | Connection accepted
1 | Connection refused, unacceptable protocol version
2 | Connection refused, identifier rejected
3 | Connection refused, server unavailable
4 | Connection refused, bad user name or password
5 | Connection refused, not authorized
Notes: What Types of Message Transfer Protocols are available ?

## Slide 7
PUBLISH PACKET
MQTT PUBLISH | 
Contains | Example
packetID | 5468
topicName | “machine1/sensor”
qos | 1
retainFlag | False
payload | “temperature: 120C”
dupFlat | false
Data Queue
Message is in payload
Multiple Publishers to the topic at the Broker
FIFO not guaranteed
Notes: What Types of Message Transfer Protocols are available ?

## Slide 8
SUBSCRIBE PACKET
MQTT SUBSCRIBE | 
Contains | Example
packetID | 5468
qos1 | 1
Topic1 | “machine1/sensor”
qos2 | 0
topic2 | “machine1/alarm”
…. | …..
Receives message from a topic
Multiple subscribers per topic
Post-Processing of Messages
FIFO not guaranteed
Asynchronous
Data Buffer at the Broker
Notes: What Types of Message Transfer Protocols are available ?

## Slide 9
Connection Flow
TCP connection
CONNECT
CONNACK
MQTT
Broker
MQTT
Client
Email Notification
TCP connection
PUBLISH
SUBSCRIBE
SUBACK
Notes: What Types of Message Transfer Protocols are available ?

## Slide 10
Message
Data element/record in the topic
Only and As sent by Publishers
Received as is by Subscribers
Contains data and optional attributes
Secure Transport
Max Size : 268435455 bytes
{
“data”: “sensor temperature”,
“attributes”:
{
“id”: 300302,
“timestamp”: 2025-01-20 23:23:32.404,
“value”: 120
}
}
Notes: What Types of Message Transfer Protocols are available ?

## Slide 11
Topic & Sub-Topics
Topic Names are Unique
UTF-8 Formatted String
Topic Levels are separated by a forward slash ‘/’
Topic names allow ‘space’ but are case sensitive
Wildcards can be used to subscribe to all sub-topics under a topic “+” or “#”
machine1/sensor/pump/#
machine1/sensor/+/temperature
machine1/sensor/pump/temperature
Notes: What Types of Message Transfer Protocols are available ?