## Slide 1
OPC-UA in Context of IIoT
Dr. Binil Starly
James T. Ryan Professor
Edward P. Fitts Department of Industrial & Systems Engineering
Notes: https://www.linkedin.com/learning/programming-foundations-databases-2/relational-databases-2?u=53565897

## Slide 2
7
OPC-UA vs Profinet
Plant Floor Level
Operations
Level
Enterprise Level
OPC UA Server
OPC UA Client
Command & Control
OPC UA Server
OPC UA Server
OPC UA Server
OPC UA Client
SCADA
Historian
OPC UA Server
OPC UA Client
BI
MES
ERP
OPC UA Client
OPC UA Client
OPC UA Client

## Slide 3
7
Profinet
Plant Floor Level
Operations
Level
Enterprise Level
OPC UA Server
OPC UA Client
Command & Control
OPC UA Server
OPC UA Server
OPC UA Server
OPC UA Client
SCADA
Historian
OPC UA Server
OPC UA Client
BI
MES
ERP
OPC UA Client
OPC UA Client
OPC UA Client

## Slide 4
7
OPC-UA
Plant Floor Level
Operations
Level
Enterprise Level
OPC UA Server
OPC UA Client
Command & Control
OPC UA Server
OPC UA Server
OPC UA Server
OPC UA Client
SCADA
Historian
OPC UA Server
OPC UA Client
BI
MES
ERP
OPC UA Client
OPC UA Client
OPC UA Client

## Slide 5
7
OPC-UA vs Profinet Summary
 | PROFINET | OPCA UA
Cycle Time | Between 0.125 – 512 ms | ~200ms, depending on server and connection
Jitter | 0.0001 – 1 ms | 10 – 100 ms
Data Format | Tightly defined data format | Object oriented complex information model
Physical Length | Limited (by Cable Length) | Unlimited
Network Boundaries | It not forwarded to network routers or jump between various networks | Specifically designed to be going through network routers and various business networks
Cyclic Data Exchange | Guaranteed Performance | Best Effort Performance

## Slide 6
7
OPC-UA vs MQTT
Pressure Gauge
MQTT Broker
MQTT Client
MQTT Client
Publish 3bar
Publish 3 bar
Publish 3 bar
MQTT Pub-Sub Pattern

## Slide 7
7
OPC-UA vs MQTT
Request-Response Pattern
+
Pub-Sub Pattern (relies on MQTT protocol)
OPC UA Server
OPC UA Client
Command & Control

## Slide 8
7
OPC-UA vs MQTT
 | OPC UA | MQTT
Communication Type | Request – Response + Pub-Sub Pattern | Only Pub-Sub Pattern
Openness | Open but must join the OPC-Foundation (a club) | Completely OPEN Protocol. Do not have to pay to use it.
Bandwidth (Data Packet) | Significant (50X than MQTT) | Low bandwidth Consumption (1X)
Unified Namespace | YES (through node addresses + tags) | YES ( through topic + tag names)
Data Format | Standard Format and hence inflexible | Unspecified Format. Subscriber must know how to decipher the format
Memory Consumption on Devices | High | Low
Data Subscribers | Limited | Almost unlimited

## Slide 9
Profinet
  Really useful for inter-device communication at short distances for real-time control
OPC/UA
  Communication with higher level IT Systems
  Can be expensive to implement
  Mainly Poll-Response mode of communication
MQTT
  Low bandwidth, memory efficient communication between devices
  Unstructured format makes it flexible and extensible
  Low cost implementation with thousands of field assets connected
In Summary