## Slide 1
Comparing Images: MSE and SSIM techniques
Dr. Binil Starly
James T. Ryan Professor
Edward P. Fitts Department of Industrial & Systems Engineering

## Slide 2
MSE vs SSIM
An image classifier that describes how similar two images are.
MSE (Mean Square Error): MSE will calculate the mean square error between each pixels for the two images
SSIM (Structure Similarity Index Measure): Checks if the pixels in the two images line up to have similar pixel density values.
The parameters include the (x, y) location of the N x N window in each image, the mean of the pixel intensities in the x and y direction, the variance of intensities in the x and y direction, along with the covariance. c1 and c2 are constants. SSIM is between -1 and 1.

## Slide 3
Mean Square Error (MSE)
(165, 156, 146)
(172, 160, 161)
REFERENCE
TEST
https://scikit-image.org/docs/dev/api/skimage.metrics.html#mean-squared-error

## Slide 4
Normalized Mean Square Error (MSE)
https://scikit-image.org/docs/dev/api/skimage.metrics.html#skimage.metrics.normalized_root_mse

## Slide 5
Structural Similarity Index Measure (SSIM)
Luminance
Contrast
Structure
k1 = 0.01; k2 = 0.03; L = dynamic range of pixel values 28 - 1
Paper: https://www.cns.nyu.edu/pub/eero/wang03-reprint.pdf
Notes: https://www.cns.nyu.edu/pub/eero/wang03-reprint.pdf

## Slide 6
MSE , Norm-MSE , SSIM
Images need to be of same size.
Images converted to Gray-Scale, although multi-channel is possible.
Useful when comparing good quality vs bad quality image.
Can tell if the images are mis-aligned.
Small defects are not identified.
Blurred or badly exposed images can be identified.
Does not detect the type of defect